## Slide 1: Amazon Picking Challenge

## Slide 2: The team
Hang Kayu
Francisco Vina
Michele Coledanchise
Karl Pauwels
Alessandro Pieropan
Danica Kragic

## Slide 3: The Key of Our System
Shelf Localization
  Front legs based
  Triangulate legs and the base_laser_link
  Position and orientation
  Human confirm to initialization
Prior updating
  Remember and update the pose of legs
  Insensitive to noise
  Recovery from occlusion
  File stream for hot backup

## Slide 4: Knowing the location of the shelf
Position of each bin is known
Define navigation waypoints to reach the shelf
Define perception/manupulation waypoints to move the arm in front of each bin
Only the last step of grasping involves some kind of reasoning

## Slide 5: Strategy
Order bins by number of objects
Pick first object on the list
Move the robot to the desired bin
Find the object in the bin
Pick the object
Drop the object

## Slide 6: Modules
Detection
Fuse camera, kinect ,laser scanner
Grasping
Reach Bin
Manipulation
Move the base
Decision
Provide Next object to grasp
Provide Position x,y,z
Compute a motion plan for the arm (MoveIt!)
Move the arm
Try different grasps
Decide whether to remove or postpone a dropped object.

## Slide 7: Behavioral trees
Easy to code
Execute External ROS nodes (C++ or Python)
Each Module should be standalone (i.e. know when to start and report if it has succeeded or not).

## Slide 8: First Design

## Slide 9: Final Design

## Slide 10: Ideal Design

## Slide 11: Perception
2 steps procedure
Object detection using Simtrack
Cloud clustering to find potential unrecognized objects

## Slide 12: Simtrack Imax

## Slide 13: Building the Point Cloud of the Bin
Shelf localization to find position of the right bin
Cloud built using Kinect and tilt laser
Crop the cloud to have points inside the bin boundaries (tuned manually)

## Slide 14: Segmentation of Objects
Iterative Euclidean clustering to fit the known number of object in the bin
Discard small clusters
Discard floating clusters

## Slide 15: The Strategy
Simtrack recognizes the right object to pick
Pick the object
  10 points in single bin
  15 points in double bin
  20 points in others

## Slide 16: The Strategy in double bin item
Simtrack recognizes the other object to pick
Segmentation finds 2 clusters
Pick the unknown cluster

## Slide 17: The Dirty Strategy
Simtrack does not recognize the object to pick
Segmentation finds as many clusters as the objects in the bin
Number of unknown clusters <= 2
Pick all the clusters
  10 points in single bin
  3 points (15 - 12) points in double bin
  8 points (20 - 12) in other bins

## Slide 18: Grasping
7 steps:
  Object detection (SimTrack + Segmentation)
  Pre-grasping (posing gripper in front of the bin)
  Reaching (reach the grasping point, i.e. object center)
  Grasping
  Prepare for retreat (lifting + centering in bin)
  Retreat (drive the robot backwards)
  Dropping

## Slide 19: Grasping
Grasping Frame:
  Based on detected object frame
  Projected such that:
    X: inward
    Y: point to right
    Z: downward
  Consistent frame for specifying grasping motion
  MoveIt receives grasping poses expressed in this frame only
object_frame
grasping_frame

## Slide 20: Grasping
Side-grasping:
  Yaw: allow +- 15 degrees freedom
  Roll: always 0
  Pitch: always 0
  Reaching distance: grasping dictionary based
Top-grasping:
  Yaw: +- 15 degrees freedom
  Roll: always 0
  Pitch: 15 – 45 degrees
  Touching: grasping dictionary based
Grasping dictionary:
  Objects dimensions
  Graspable faces
  Detection methods
  Top/Side grasping

## Slide 21: PR2 Limitations
Torso is very slow to raise
Hand is very large
Cannot reach the top level
Cannot grasp wide or flat objects

## Slide 22: What went wrong in Seattle
PR2 provided by Clearpath
Little time to calibrate it
Lighting condition