## Slide 1: Amazon Picking Challenge

## Slide 2: The team
Current and past affiliations here
Hang Kaiyu: Grasping
Francisco Vina, Grasping and PR2 Specialist
Michele Colledanchise, Behavioral Trees
Karl Pauwels, Computer
Alessandro Pieropan, Computer Vision and project leader
Prof. Danica Kragic

## Slide 3: The Robot
Torso is very slow to raise ( 30 seconds)
Hand is very large making grasping very hard in the bins
Cannot reach the top level of the shelf
Cannot grasp wide or flat objects

## Slide 4: Strategy
Tasks ordered by number of objects in bins and level of shelf
Non graspable objects are removed from the queue
Bins with 3 or more objects left at the end
Move the robot to the desired bin
Find the object in the bin and grasp it
Pick the object
Drop the object

## Slide 5: Shelf Localization
Base Laser scanner
  Point cloud clustering to find legs
  Triangulate legs and the base_laser_link
  Position and orientation
  Remember and updates the position of the legs
  Robust to noise
  Recovers from occlusion

## Slide 6: Definition of waypoints
Position of each bin is known
Define navigation waypoints to reach the shelf
Define perception/manupulation waypoints to move the arm in front of each bin
Only the last step of grasping involves some kind of reasoning

## Slide 7: Behavior trees
Easy to develop and test
Execute External ROS nodes (C++ or Python)
Each Module should be standalone (i.e. know when to start and report if it has succeeded or not).

## Slide 8: Final Design
?
List of Object Empty
Detect Object
Next
Object from List
Drop
Object
Grasp Object
Remove
Object from List
→
Base, Torso, Head, Init
→
Pre-Grasp
?
Incrementally added more functionalities
(initialization and pre-grasp poses)
If some action fails (we cannot deal with that object),
we the put the object at the end of the list of objects to pick
(we will try again later)
If the list of objects to pick is not empty: Detect, Grasp, Drop Object
and then go to the next object

## Slide 9: Ideal Design
?
List of Object Empty
Base, Torso, Head, Init
Remove
Object from List
Object Position Known
Detect Object
?
→
Object Grasped
?
Object possible to recover
Append Object
to List
→
Object Dropped
Drop
Object
?
Grasp Object
→
Pre-Grasp
Object impossible to recover
Remove
Object
From List
→
The ideal design is more reactive
And handles better the action failures

## Slide 10: Perception
2 strategies
Object detection and 6DOF estimation using Simtrack
Cloud clustering to find potential unrecognized objects

## Slide 11: Building the Point Cloud of the Bin
Shelf localization to find position of the right bin
Cloud built using Kinect and tilt laser scanner on the torso
Crop the cloud to have points inside the bin boundaries
Iterative Euclidean clustering to fit the known number of object in the bin

## Slide 12: Grasping
7 steps:
  Object detection (SimTrack + Segmentation)
  Pre-grasping (posing gripper in front of the bin)
  Reaching (reach the grasping point, i.e. object center)
  Grasping
  Prepare for retreat (lifting + centering in bin)
  Retreat (drive the robot backwards)
  Dropping

## Slide 13: Grasping
Side-grasping:
  Yaw: allow +- 15 degrees freedom
  Roll: always 0
  Pitch: always 0
  Reaching distance: grasping dictionary based
Top-grasping:
  Yaw: +- 15 degrees freedom
  Roll: always 0
  Pitch: 15 – 45 degrees
  Touching: grasping dictionary based
Grasping dictionary:
  Objects dimensions
  Graspable faces
  Detection methods
  Top/Side grasping

## Slide 14: What went wrong in Seattle
PR2 provided by Clearpath
Little time to calibrate it
Lighting condition